## Slide 1
Smart India Hackathon 2026 · Intelligent Dead Reckoning
SMART INDIA HACKATHON 2026
Intelligent Dead Reckoning
A phone that keeps a vehicle on the map when GNSS goes dark: tunnels, underpasses, multi-level parking and urban canyons. Fully offline, no server, no extra hardware.
PROBLEM STATEMENT ID
SIH26168
PROBLEM STATEMENT TITLE
AI-based dead reckoning for vehicle positioning in GNSS-denied environments
THEME
Smart Vehicles
PS CATEGORY
Software
TEAM ID
420
TEAM NAME
Odyssey
TUNNEL
drift
GNSS
IMU only
Map-snapped
Three tracks drawn live on the phone. Blue is GNSS, orange is the IMU integrating alone, green is the estimate snapped to the offline road graph. The gap between orange and green is what the tunnel costs.

## Slide 2
Idea & Proposed Solution
Smart India Hackathon 2026 · Intelligent Dead Reckoning
2 / 6
THE PROBLEM
GNSS fails exactly where a driver needs it most: tunnels, underpasses, flyover stacks, parking decks and dense urban canyons.
Consumer navigation freezes or jumps to a wrong road, and recovers only after the sky is back.
The phone's own IMU can bridge the gap, but drifts by tens of metres within a minute if it is left to integrate on its own.
OUR SOLUTION
An Android app that fuses the phone's IMU, GNSS and an offline OpenStreetMap road graph, shifting trust from satellites to inertial sensing before the fix is lost, and snapping the drifting estimate back onto the road so the vehicle never leaves the map.
HOW IT DIFFERS
100% offline
No server, no API key
No extra hardware
Measured, not assumed
1
Strapdown inertial integrator
Attitude from the rotation vector, acceleration levelled into ENU, gravity and bias learned on the device. Zero-velocity updates pin drift at every stop.
2
GNSS trust gate
Satellite count and C/N0 collapse before fixes stop. The filter hands over to the IMU on that early evidence instead of waiting for a timeout.
3
On-device HMM map matching
A Viterbi matcher snaps the estimate to the road and feeds the road bearing back as a heading observation. Heading error stops accumulating.
4
Road graph rebuilt on the phone
Mapsforge vector tiles carry no connectivity. We recover it by snapping endpoints on a half-metre grid, so no routing server is needed, even underground.

## Slide 3
Technical Approach
Smart India Hackathon 2026 · Intelligent Dead Reckoning
3 / 6
1
Phone sensors
Accel, gyro, mag, rotation vector, barometer at 200 Hz; GNSS + satellite status at 1 Hz
2
Levelling & ZUPT
Rotate into ENU, remove learned gravity and bias, zero-velocity update when parked
3
Strapdown integrator
10 Hz position and velocity; re-anchored to GNSS only while the fix is healthy
4
HMM map matcher
Viterbi over the on-device road graph; matched bearing fed back as heading
5
Along-road tracker
Position as a scalar along the road polyline during an outage; road supplies direction
6
Offline map UI
osmdroid + Mapsforge vector maps; GNSS, IMU and snapped tracks drawn live
heading feedback: matched road bearing corrects the integrator
TECHNOLOGY STACK
Mobile
Kotlin, Android foreground service, single-writer sensor thread, 2 s flush so a crash costs at most two seconds
Maps
osmdroid + Mapsforge vector .map files (OpenStreetMap data, ODbL). In-app zone downloader for all of India
AI / ML
PyTorch 1-D ResNet speed head exported to TorchScript Mobile; 40 ms per inference on a dedicated thread
Fusion
Strapdown INS + ZUPT + scalar Kalman gain on model speed; HMM Viterbi map matching; along-road tracking
Evaluation
Python harness: CRSE, CAE, AEPS on synthetic outages cut from recorded drives, scored against GNSS truth
ON-DEVICE EXECUTION
Thread
Owns
Rate
imu-logger
Sensor + GNSS callbacks, all file writes, integrator
200 Hz
imu-ml
Model load and inference
10 Hz
map-match
Tile reads, HMM matcher, road graph
0.5 Hz
Exactly one writer thread, no locks. Inference results are posted back to the logger thread; stale requests are dropped rather than queued. GNSS is trusted only with 4+ satellites used and accuracy under 20 m.

## Slide 4
Feasibility & Viability
Smart India Hackathon 2026 · Intelligent Dead Reckoning
4 / 6
MEASURED ON DEVICE: POSITION ERROR DURING SYNTHETIC GNSS OUTAGES
Chart: mean error, m (CRSE)
| 10 s outage | 30 s outage | 60 s outage
Dead reckoning + heading feedback (live today) | 10.2 | 36 | 87.5
Along-road, fed integrator distance | 12.6 | 40.8 | 104.7
Along-road, fed true distance | 8.3 | 22.3 | 50.5
46 to 57 outages per duration, cut from recorded sessions and scored against GNSS ground truth. Along-road tracking cuts 60-second error by 42% once it is fed a trustworthy distance.
WORKING TODAY
✓
Android app records 11 sensor streams on a Samsung Galaxy S21 FE, time-aligned on one monotonic clock
✓
Dead reckoning with map-matched heading feedback runs on the phone and is measured, not simulated
✓
Road topology recovered on device: 25,383 segments around IIT Kharagpur, 100% linked, 98.5% in one component
✓
Offline maps render with no tile server; zones for the rest of India download in-app
CHALLENGES & HOW WE CLOSE THEM
Along-track bias
A -0.02 m/s² acceleration bias costs ~30% of distance over 60 s unaided. Fix: learn horizontal bias against GNSS velocity while the fix is healthy, carry it into the outage.
Under-trained speed model
304 training windows, walking pace only. Fix: record vehicle-speed drives, retrain, and enable speed fusion only if it beats a constant predictor.
Map size and field validation
The 210 MB zone map ships as a release asset with an in-app downloader. Heading feedback has run only in replay; next step is a live road test.

## Slide 5
Impact & Benefits
Smart India Hackathon 2026 · Intelligent Dead Reckoning
5 / 6
0
cloud calls, servers or API keys
10 Hz
position updates on the handset
42%
lower 60 s outage error with along-road tracking
100%
of India coverable with free OSM zone maps
Social
Drivers, ambulances and delivery riders keep guidance through tunnels, underpasses and hill-road cuttings
No wrong turn at a tunnel exit: the position is already on the right road when the sky returns
Works on the phone people already own; nothing to buy or install in the vehicle
Economic
Zero recurring cost: no map API billing, no data plan, no server to run
Fleet and logistics tracking that does not go blind under flyovers or in parking decks
One codebase for OEM navigation, ride-hailing and toll or road-agency apps
Strategic & Environmental
Location never leaves the device: privacy by construction
Offline by design, so it serves low-connectivity and remote regions first, not last
Fewer missed exits and detours means less fuel burnt; road topology from OSM is open and reusable
Scalability. One Mapsforge file per zone (210 MB for eastern India, 1.5 GB for the whole country). The same estimator extends to metro and rail, indoor parking and two-wheelers, and its measured outage harness lets every future change be gated on numbers.

## Slide 6
Research & References
Smart India Hackathon 2026 · Intelligent Dead Reckoning
6 / 6
LITERATURE WE BUILD ON
Brossard, Barrau, Bonnabel (2019). AI-IMU Dead-Reckoning. arXiv:1904.06064
Hurwitz, Cohen, Klein (2024). Deep Learning Assisted Inertial Dead Reckoning and Fusion. arXiv:2407.16387
Gomes, Costa (2020). Vehicular Dead Reckoning Based on Machine Learning and Map Matching. IEEE
Suwandi, Kitasuka, Aritsugi (2019). Vehicle Vibration Error Compensation on IMU-accelerometer Sensor Using Adaptive Filter and Low-pass Filter Approaches. J. Inf. Processing 27
Nirmal et al. (2016). Noise modeling and analysis of an IMU-based attitude sensor. arXiv:1608.07053
Chao et al. (2022). A Comprehensive Review of Map-Matching Techniques. Int. J. Web Services Research 19(1)
Newson, Krumm (2009). Hidden Markov Map Matching Through Noise and Sparseness. ACM SIGSPATIAL
IO-VNBD (Coventry Univ.). Inertial and Odometry Vehicle Navigation Benchmark Dataset for model training and CRSE / CAE / AEPS metric definitions
EXISTING SOLUTIONS STUDIED
Google Maps SDK
No offline tile access, no dead-reckoning hook, billing account required. We use OSM data under ODbL instead.
OSRM-based map matching
Accurate, but needs a routing server. We rebuild road connectivity on the handset from Mapsforge tiles.
Learned inertial odometry (RoNIN, AI-IMU)
Strong results with dense training data. Our speed head reuses the idea but is gated until it beats a constant.
Open data and tools. OpenStreetMap (ODbL), Mapsforge map builds, osmdroid, PyTorch Mobile, Android Sensor and GNSS status APIs. Every number in this deck is reproducible from the committed evaluation harness against recorded sessions.